## Slide 1: Sound sources
Tyler Dare
Nonlinear sources

## Slide 2: Nonlinear sources
Up to now, we assume the forcing function is independent of the response:
  Piston’s motion does not depend on acoustic field
  Force on mass does not depend on the mass’s motion
In some systems, the response affects the excitation and the excitation causes the response.
  Microphone picks up the sound from a speaker, which amplifies the sound further, leading to feedback

## Slide 3: Friction-induced vibration
Friction force can vary with velocity.

## Slide 4: Friction-induced vibration
What is the behavior of a SDOF system excited by a friction force?

## Slide 5: Friction-induced vibration
In general, the friction force is a function of the relative velocity between two surfaces.

## Slide 6: Friction-induced vibration
Static and dynamic friction coefficients can be significantly different.

## Slide 7: Friction-induced vibration
Modeling can be easier if we smooth the function out.

## Slide 8: Friction-induced vibration
What is the behavior of a SDOF system excited by a friction force?

## Slide 9: Friction-induced vibration
Taylor series:

## Slide 10: Friction-induced vibration
Friction acts like additional damping, but it can also be negative!

## Slide 11: Friction-induced vibration

## Slide 12: Friction-induced vibration

## Slide 13: Friction-induced vibration

## Slide 14: Friction-induced vibration

## Slide 15: Friction-induced vibration
Vibrations grow if:
  The system’s damping dissipates energy faster than friction adds it
Vibrations decay if:
  Friction adds energy faster than the system can dissipate it
Stick-slip can occur when the friction is decreasing with increasing speed.

## Slide 16: Vortex shedding and lock-in
Large oscillations can occur when flexible structures are excited by flow.

## Slide 17: Vortex shedding
Cesareo de La Rosa Siqueira
Oscillating vortices in flow behind an object.

## Slide 18: Non-dimensional quantities
Expressing variables in terms of non-dimensional quantities helps us characterize the physics in general. We use non-dimensional quantities in acoustics:
“frequency ratio”: how fast is the excitation compared to resonance
“damping ratio”: how heavily damped is the structure
“transmissibility”: what fraction of the force is transmitted through a mount

## Slide 19: Non-dimensional quantities in fluid dynamics
Fluid dynamicists love non-dimensional quantities. The most important one is:
Reynolds number:
  : Flow speed
  : Characteristic length
  : Kinematic viscosity of the fluid
  : Dynamic viscosity (usually just called “viscosity”)
  : Density
Fluid at C | , Pas | , | ,
Air |  |  | 
Water |  |  | 
Air |  |  | 
Water |  |  | 

## Slide 20: Non-dimensional quantities in fluid dynamics
Reynolds number:
  : Flow velocity
  : Characteristic length
  : Kinematic viscosity of the fluid
Reynolds number represents:
  The ratio of inertial forces to viscous forces within a fluid
  How “big and fast” something is compared to how viscous the fluid is
  How “complex” the flow is
Whale swimming:
Bacterium swimming:
Osborne Reynolds
Low Re
High Re

## Slide 21: Vortex shedding
For a cylinder in a cross-flow, the Reynolds number determines what happens to the downstream flow:
For a wide range of Reynolds numbers, vortex shedding occurs.
By Teapeat - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=23285699
Cesareo de La Rosa Siqueira

## Slide 22: Vortex shedding
The frequency of the shed vortices is described in another non-dimensional quantity, the Strouhal number:
: Vortex shedding frequency
: Characteristic length
: Flow speed
Cesareo de La Rosa Siqueira

## Slide 23: Vortex shedding
The Strouhal number is fairly constant across a very wide range of Reynolds numbers
for cylinders for many flow conditions
Cesareo de La Rosa Siqueira

## Slide 24: Vortex shedding
For a cylinder of length and diameter , with flow velocity , the shedding frequency is
This produces a dipole-like source:
Cesareo de La Rosa Siqueira

## Slide 25: Vortex-induced vibration
The shed vortices also produce oscillating lift on the cylinder.
Cesareo de La Rosa Siqueira

## Slide 26: Vortex-induced vibration
https://www.youtube.com/watch?v=Eh_vOcXazaU

## Slide 27: Vortex-induced vibration
M.L. Facchinetti et al. / Journal of Fluids and Structures 19 (2004) 123–140
Just like friction-induced vibrations, there is a competition between:
  The energy the fluid adds to the structure
  The energy the damping removes from the structure
If the structure cannot dissipate all of the energy, large oscillations can occur.

## Slide 28: Vortex-induced vibration and lock-in
Lock-in is a high-amplitude vibration that can occur when the vortex shedding frequency is close to the resonance frequency. The shedding frequency “locks-in” to the resonance frequency and tends to stay there, even if the flow speed is changed.
Lock-in occurs because the system cannot dissipate energy fast enough at low amplitudes. The oscillations grow until:
  There is enough drag on the body to dissipate the energy, or
  Something breaks

## Slide 29: Reducing vortex shedding and lock-in
Shedding will be louder if the cylinder is longer
  Make the cylinder function as multiple shorter cylinders by adding strakes
  Coherent length: distance over which sources are coherent
By StromBer - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=14871163

## Slide 30: Reducing vortex shedding and lock-in
By StromBer - Own work, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=14871163
Robert Blevins, Harris’ Shock and Vibration Handbook, 6th ed., Ch 30

## Slide 31: Reducing vortex shedding and lock-in
Changing the shape of the trailing edge of a body in flow can significantly reduce the vortex shedding and lock-in risk.
Worse
Better
W.K. Blake, “Excitation of Plates and Hydrofoils by Trailing Edge Flows,” J. Vib., Acs., Stress, and Reliability in Design, 1984.
Baseline

## Slide 32: Aeroelasticity and the Tacoma Narrows Bridge
For a 2-D shape, the fluid can cause pitching as well as lift
The twisting motion follows the equation:
  and depend on the speed and geometry.
  Negative damping occurs if
See videos at https://en.wikipedia.org/wiki/Tacoma_Narrows_Bridge_(1940)
Billah and Scanlan, Resonance, Tacoma Narrows bridge failure, and undergraduate physics textbooks, Am. J. Phys 59 (2), 1991