## Slide 1: Acoustic Enclosures
Tyler Dare
Sabine rooms

## Slide 2: Modal overlap
At high enough frequency, talking about individual modes is less useful. Many modes are participating at a given frequency.

## Slide 3: Modal overlap
Number of modes with resonances less than is approximated by:
where is volume, is total surface area, and is the length of all of the edges.
Modal density is the number of modes in a narrow frequency band,

## Slide 4: Modal overlap

## Slide 5: Sabine room
A Sabine room is one where we can treat the sound field as diffuse.
  Sound pressure is assumed to be the same everywhere, except very near the source.
  Sound waves are assumed to arrive from random directions.
Requirements:
  At least 3–6 modes in the frequency band of interest.
  Modal overlap should be at least 3.
  Walls must be locally-reacting.

## Slide 6: Sabine room
Pressure level in a Sabine room is
In air, far from a source,
Where is the room constant

## Slide 7: Room constant
Room constant
is the average absorption coefficient, weighted by area
Absorption coefficients for common materials can be found in tables, often from material suppliers.

## Slide 8: Directivity factor
The directivity factor is a property of how directional the source is. For omnidirectional sources,
  if the source is far from any reflecting surfaces
  if the source is near (within ) a hard wall
  if the source is near two hard walls
  if the source is near a corner

## Slide 9: Direct and reverberant fields
If a receiver is in the direct field of a source, adding absorption will not be very beneficial.

## Slide 10: Example problem: adding treatment
Room 10 m 10 m 5 m
Machine in the center of the floor and operates at 250 Hz.
All surfaces have absorption
How much quieter will the room be if the walls and ceiling are treated with absorbing material with ?

## Slide 11: Example problem: adding treatment
Room 10 m 10 m 5 m
Machine in the center of the floor and operates at 250 Hz.
All surfaces have absorption
How much quieter will the room be if the walls and ceiling are treated with absorbing material with ?

## Slide 12: Example problem: adding treatment
Room 10 m 10 m 5 m
Machine in the center of the floor and operates at 250 Hz.
All surfaces have absorption
How much quieter will the room be if the walls and ceiling are treated with absorbing material with ?

## Slide 13: Example problem: adding treatment
Room 10 m 10 m 5 m
Machine in the center of the floor and operates at 250 Hz.
All surfaces have absorption
How much quieter will the room be if the walls and ceiling are treated with absorbing material with ?

## Slide 14: Measuring the room constant
The average absorption can be calculated from reverberation time,

## Slide 15: Example problem: treatment options
A room is 10 m 15 m 6 m high. The room currently contains several machines and workers. Four new machines are to be installed. You are tasked with making sure the new machines do not bring the overall sound levels above 85 dB.
The machines are available in two models:
  “Loud”, which produce sound power of 94 dB re: 1 pW
  “Quiet”, which produce sound power of 84 dB re: 1 pW, but cost $1,600 more each
What measurements must be done? What treatment options are available if the levels are too high? What is the most cost-effective solution?

## Slide 16: Example problem: treatment options
Step 1: baseline measurements
  Measure existing sound pressure levels with the other machines on
  Measure reverberation time with the machines off
  Calculate volume and area

## Slide 17: Example problem: treatment options
Step 2: calculate baseline conditions

## Slide 18: Example problem: treatment options
Step 3: initial predicted level
dB re: 20 Pa

## Slide 19: Example problem: treatment options
Explore other options
  What if we bought the loud machines and then spent money on absorbing material?
  Acoustic tile with is $3 per square meter.

## Slide 20: Example problem: treatment options
Explore other options
  Acoustic tile with is $3 per square meter.
  Covering the ceiling in acoustic tile would cost $450

## Slide 21: Octave bands
If a source acts at multiple octave or one-third octave bands, treat them as separate sub-problems, then add all of the energy together (combine levels) at the end.