## Slide 1: Vibration isolation
Tyler Dare
Practical considerations and measurements

## Slide 2: Specifying isolators
Spring elements often specified with maximum load and deflection.
From Kinetics Noise Control

## Slide 3: Specifying isolators
Spring elements often specified with maximum load and deflection.
From Kinetics Noise Control

## Slide 4: Types of isolators
Actual response of a given material depends on geometry, configuration, machine’s mass, etc.
But different types of isolators tend to be used more often in different frequency ranges
1 Hz
10 Hz
100 Hz
250 mm
2.5 mm
0.025 mm
Maximum deflection
Operating frequency
Air springs
Metal springs
Rubber and elastomers
Cork and felt pads

## Slide 5: Air springs
Air springs can be used at very low frequencies, down to 1 Hz or less.
From Firestone Airride

## Slide 6: Metal springs
Metal springs have very low internal damping, so either avoid resonance or include a damping element in parallel.
From Kinetics Noise Control

## Slide 7: Surging in springs
“Surging” occurs where longitudinal resonances form in the spring coil. Isolation is much less effective above these frequencies.
Surging frequencies occur at
From Kinetics Noise Control

## Slide 8: Wire rope isolators
Coiled wire ropes act as springs and also provide damping due to friction between strands.
Nonlinear effects can occur, so make sure to test after installation.
From Isolation Dynamics Corp.

## Slide 9: Rubber isolators
Dynamic stiffness can be 1.3–1.8 times static stiffness, so dynamic data is needed for isolation predictions.
Damping depends on specific type of rubber and chemistry.
Different stiffness in shear vs. compression
Generally not used in tension due to fatigue damage
From Kinetics Noise Control

## Slide 10: Pads
Isolation pads are easy to install.
Stiffness depends on material, thickness, and geometry.
Cork and felt can have stiffness dependent on frequency and preload.
From Kinetics Noise Control
From Kinetics Noise Control

## Slide 11: Four-isolator systems
6 DOF motion is possible for rigid body
Imbalanced mass load will force horizontal and vertical directions equally.
Need to consider lateral stiffness of isolators.

## Slide 12: High-frequency response
At high frequencies, the resonances of the structure being isolated will start to matter.
The vibrating structure will generate sound, even though force is not being transmitted to the foundation.
Isolation is generally ineffective at reducing audible frequencies.

## Slide 13: Designing a mounting system
A machine in a factory is shaking the floor and disrupting other work. Design an isolation mount to reduce the vibration of the floor.
Machine
Machine
Mount

## Slide 14: Measuring isolation performance
Insertion loss: change in level with and without mounts
Transmission loss: change in level above and below mounts
Modified transmission loss: change in level compared to free vibration
Machine
Mount

## Slide 15: Measuring vibration
Accelerometers output voltage proportional to acceleration.
Piezoelectric accelerometers are the most common for industrial and scientific applications.
Accelerometers from PCB Piezotronics

## Slide 16: Measuring vibration
Piezoelectric crystals produce a small electrical charge proportional to pressure.
Integrated circuitry amplifies the signal and converts it to a voltage usable by the data acquisition system.
The DC component (constant acceleration) is usually (but not always) filtered out.
Mass
Crystal
Amp
Diagram from PCB Piezotronics

## Slide 17: Accelerometer response
The accelerometer system acts as a multi-DOF oscillator. The output is related to the compression of the crystal.
Mass
Crystal
Amp

## Slide 18: Accelerometer response
Diagram from PCB Piezotronics

## Slide 19: Predicting isolation performance
Isolation performance depends on properties of the source, isolation system, and foundation.
We can measure these components independently:
Source impedance:
  “Force source”: is low, force from machine does not change with foundation
  “Velocity source”: is high, velocity at attachment does not change with foundation
Mount impedance:
  Impedance across mount with one side blocked
Foundation impedance:
  Impedance of foundation with force and velocity at the same point

## Slide 20: Predicting isolation performance
Machine
Mount
Machine
Fixed foundation
Machine
Mount
Test 1B: Free velocity
Test 1A: Blocked force
Test 2: Mount impedance
Test 3: Foundation impedance

## Slide 21: Predicting isolation performance
Insertion loss: change in level with and without mounts
Transmission loss: change in level above and below mounts
Modified transmission loss: change in level compared to free vibration

## Slide 22: Applying known forces: shakers and instrumented hammers
An instrumented hammer is more useful when:
  You want to learn about the free response of a structure
  The structure is expected to have a linear response in the frequency and amplitude range of interest
  The structure does not permit easy or fast mounting of a shaker
A shaker is more useful when:
  You want to learn about the response due to a particular load
  You suspect the structure has a nonlinear response
  You want to learn about the change in response over time
Kistler.com

## Slide 23: Selecting the hammer size and tip material is crucial.
PCB.com
PCB.com
Kistler.com
Kistler.com
bksv.com

## Slide 24: Selecting the hammer size and tip material is crucial.
More energy
Higher frequency range

## Slide 25: Selecting the hammer size and tip material is crucial.
PCB.com
Tips of varying hardness

## Slide 26: Choosing a hammer tip

## Slide 27: Choosing a hammer tip
Harder tip
Harder tip

## Slide 28: Double hits cause a scalloped appearance in the frequency domain.

## Slide 29: Double hits cause a scalloped appearance in the frequency domain.
Moderately damped structure
Hammer

## Slide 30: Structures with low damping can make double hits difficult to avoid.
Lightly damped structure
Hammer

## Slide 31: Structures with low damping can make double hits difficult to avoid.

## Slide 32: Shaker selection depends on size and frequency range.
Wilcoxon F4/F7
wilcoxon.com

## Slide 33: Shaker selection depends on size and frequency range.
Brüel & Kjær Type 4810
bksv.com

## Slide 34: Mount shakers with a stinger, and monitor applied force with force gauge or impedance head.
Ward, Frederick, “Comparing steady state and impulse test methods to measure the damping of composites applied to homogeneous substrates”, Proc. INTER-NOISE 2018.
Zehme, John, “Evaluating Damping Treatments using Radiated Sound Power normalized by Input Mechanical Power”, Proc. INTER-NOISE 2018.

## Slide 35: Choosing shaker excitation signal
Gaussian random noise
  Should be your go-to signal for most measurements.
  Easy to get plenty of averages.
  Energy input depends on frequency range. Filter to get more energy in a certain band.
Swept sine wave
  Takes longer to get enough averages.
  Can get more energy at each frequency.
  Easier to detect nonlinearities in the system.
Play-back of previously recorded measurement