## Slide 1: Rotating machinery
Tyler Dare
Propellers

## Slide 2: How to make a quiet submarine
Log (Frequency)
SPL, dB
Rotor Inflow Turbulence Interacting with Rotor LE
Dominant Sources of Rotor Excitation
(curves represent direct radiation – proportional to force)
Blade Boundary Layer Turbulence Interacting with Rotor Blade TE
Rotor Spatial Inflow Distortions Generating Rotor Unsteady Lift
Dominant Vibrating and Radiating Structures
Vehicle Shell
Low Frequency
Propulsor
Mid Frequency
Rotating Blades
High Frequency
Cavitation

## Slide 3: Propeller noise
Rotor noise is a dominant mechanism in many systems:
  Boats, ships, and submarines
  Airplanes
  Helicopters
  Wind turbines
  Fans
Noise from rotors takes one two paths:
  “Direct noise”: unsteady flow causes acoustic fluctuations
  “Re-radiated noise”: unsteady flow causes vibrations, then vibrating structure radiates sound

## Slide 4: Propeller noise sources
Noise from propellers has tonal and broadband features.
Broadband noise is caused by turbulence
  Ingested turbulence
  Self-generated turbulence
Tonal noise (also just called “blade rate noise”) is caused by blades interacting with large flow structures
  Ingested wakes
  Self-generated vortices

## Slide 5: Turbulence ingestion noise
A source of turbulence is somewhere upstream of the rotor
The turbulence causes unsteady forces to be applied to the propeller. The excitation depends on:
  Amplitude of the fluctuating velocities
  How the blade responds to fluctuating velocity (“gust response”)
  How large the vortices are (“correlation length”)
By C. Fukushima and J. Westerweel, Technical University of Delft, The Netherlands - Own work, CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=3082535

## Slide 6: Turbulence ingestion noise
TI noise has been measured in wind and water tunnels.
TI noise tends to be the dominant source of broadband noise below a few times the blade passage frequency.
The turbulence parameters can be hard to quantify and predict.
It is still the subject of research.

## Slide 7: Self-generated turbulence noise
Also called “boundary layer turbulence noise” or “trailing edge noise”
Turbulence forms over the rotor itself.
When turbulence reaches the trailing edge, the eddies are suddenly able to expand or contract, causing noise.
Excitation depends on turbulence parameters and blade geometry.
TE noise tends to be the dominant source at higher frequencies.

## Slide 8: Trailing edge treatments
Trailing edge serrations reduce the turbulence correlation length
https://www.youtube.com/watch?v=YAl9PR6U63k

## Slide 9: Ingested blade-rate noise
An obstruction upstream causes a change in flow
The change in flow causes unsteady forces on the rotor each time a blade passes.
Similar to an impulsive source, harmonics are usually also seen.

## Slide 10: Ingested blade-rate noise
Straight wakes meeting straight blades can make blade rate noise very loud.
Kim, Geon-Seok, “Discrete-Frequency and Broadband Noise Radiation from Diesel Engine Cooling Fans,” Ph.D. Thesis in Acoustics, The Pennsylvania State University, December 2007.
Engine
Radiator
Finger guard
Shroud
Spider (Hub)
Rotation
Leading edge
Trailing edge
Blade tip

## Slide 11: Ingested blade-rate noise
Removing the upstream obstruction to make the incoming flow more uniform.
Kim, Geon-Seok, “Discrete-Frequency and Broadband Noise Radiation from Diesel Engine Cooling Fans,” Ph.D. Thesis in Acoustics, The Pennsylvania State University, December 2007.

## Slide 12: Ingested blade-rate noise
Adjust the shape of the blades (skew) to spread out the interactions in time.
Kim, Geon-Seok, “Discrete-Frequency and Broadband Noise Radiation from Diesel Engine Cooling Fans,” Ph.D. Thesis in Acoustics, The Pennsylvania State University, December 2007.
1xBR Dominated by Tip/Shroud Opening Interaction

## Slide 13: Self-generated blade-rate noise
Wings and blades generate large-scale, relatively stable vortex structures.
If one blade leaves a vortex behind, the following blade can impact it, leading to blade rate tones.

## Slide 14: Self-generated blade-rate noise
Tip vortex
https://www.youtube.com/watch?v=AolOz2AkpiE

## Slide 15: Reducing propeller noise
Reducing tip speed makes all mechanisms quieter
  Larger fans are usually quieter for the same volumetric flow rate
Clean, wake-free inflow reduces turbulence ingestion and ingested wake noise
  Avoid installing duct fans near bends and grilles

## Slide 16: Commercial fans and blowers
Tube axial fan: flow is along the axis of rotation, just a propeller in a tube. Dominated by low frequency noise.
Vane axial fan: Tube axial, but with downstream guide vanes for higher efficiency. Fan can run slower, but downstream wakes increase mid-high frequency noise.
Centrifugal fan: Flow turns 90° through the fan. Generally quieter than axial fans.
https://www.greenheck.com/products/air-movement/fans/

## Slide 17: Commercial fans and blowers
Shape of blades in centrifugal fans can affect noise generation.
https://blog.softinway.com/understanding-the-characteristics-of-varying-centrifugal-blower-designs/
High-pressure applications
Maximum efficiency, minimum noise
High volume flow rate, high pressure, loud
Generate high flow rates, quiet
By EagleX - Own work, CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=12753938

## Slide 18: Wind turbine noise
Trailing-edge noise is the dominant generation mechanism.
Trailing-edge noise can be reduced by
  Serrations: reduce coherent length
  Airfoil shaping: reduce turbulence formation
  Brushes and porous surfaces: reduce abrupt transition at trailing edge (impedance matching)

## Slide 19: Wind turbine noise
Measuring wind turbine noise can be challenging.
Both the source and propagation to the ground depends strongly on atmospheric conditions.
Blade rate tones
Indoor room mode
Zajamšek, B.; Hansen, K.L.; Doolan, C.J.; Hansen, C.H. Characterisation of wind farm infrasound and low frequency noise. J. Sound Vib. 2016, 370, 176–190

## Slide 20: Toroidal Mobius propellers revisited
The authors claim a significant noise reduction.
How is this reduction achieved?

## Slide 21: Toroidal Mobius propellers revisited
Blade rate noise: significantly reduced compared to baseline
Low-frequency noise: increased (more TI noise)
High-frequency broadband: reduced (reduced TE coherent length?)

## Slide 22: Toroidal Mobius propellers revisited
Baseline straight blades would cause wake noise from interaction with straight struts.
It would be more fair to compare curved blades without loops to curved blades with loops.

## Slide 23: Toroidal Mobius Loop propellers revisited
Better experimental design: single propeller with minimal wake interference.
Include background and motor noise measurements

## Slide 24: Toroidal Mobius Loop propellers revisited

## Slide 25: Toroidal Mobius Loop propellers revisited